## Slide 1
Subject : Microwave Theory and Techniques
By: Gaurav Vijay Topre (10303320181137210017)
Measurement Instruments: Slotted Line and Tunable Detector
Presentation on

## Slide 2
Contents
This presentation consists of
  Introduction to Microwave Bench Measurement
  Setup of Microwave Bench General Measurement
  Slotted Line
  Tunable Detector
  Advantages of using this Technique
  References

## Slide 3
Introduction
Among the Microwave measurement devices, a setup of Microwave bench, which consists of Microwave devices has a prominent place. This whole setup, with few alternations, is able to measure many values like guide wavelength, free space wavelength, cut-off wavelength, impedance, frequency, VSWR, Klystron characteristics, Gunn diode characteristics, power measurements, etc.
The output produced by microwaves, in determining power is generally of a little value. They vary with the position in a transmission line. There should be an equipment to measure the Microwave power, which in general will be a Microwave bench setup.

## Slide 4
SETUP OF
BENCH MEASUREMENT
TECHNIQUE
Fig: Setup of Microwave Bench Measurement

## Slide 5
Removes signal that is not required
Isolator
  the signal can be adjusted to its resonance frequency using this
  provision to couple the signal to waveguide
Frequency Meter
Crystal Detector
  used to demodulate the signals
  Generating signals in milliwatts
  E.g Gunn diode oscillator or a Reflex Klystron tube
Signal Generator
  Select Desirable Frequency
  Confines the o/p in range 0 to 50db
Precision Attenuator
Variable Attenuator
  This sets amount of attenuations
Standing Wave Indicator
  provides the reading of standing wave ratio in dB

## Slide 6
A slotted line carriage is a microwave instrument which is used to measure:
• Wavelength
• Voltage Standing Wave Ratio (VSWR) and standing wave pattern
• Impedance, reflection coefficient and return loss measurement
SLOTTED LINE

## Slide 7
• It has a coaxial E-field probe which penetrates inside a rectangular waveguides slotted in sections from the outer wall.
• The probe is able to transverse a longitudinal narrow slot and locate the standing waves maxima(Vmax) and minima (Vmin) along the line giving VSWR.
Construction:
The slotted line consists of a slotted section of a transmission line, where the measurement has to be done. It has a travelling probe carriage, to let the probe get connected wherever necessary, and the facility for attaching and detecting the instrument.
In a waveguide, a slot is made at the center of the broad side, axially. A movable probe connected to a crystal detector is inserted into the slot of the waveguide.
Fig: Standing wave patterns on a line for various reflection coefficients showing maxima and minima

## Slide 8
Parts labelled in figure are as follows
Operation
The output of the crystal detector is proportional to the square of the input voltage applied. The movable probe permits convenient and accurate measurement at its position. But, as the probe is moved along, its output is proportional to the standing wave pattern, which is formed inside the waveguide. A variable attenuator is employed here to obtain accurate results.
Output VSWR can be obtained by equation
1. Launcher − Invites the signal.
2. Smaller section of the waveguide.
3. Isolator − Prevents reflections to the source.
4. Rotary variable attenuator − For fine adjustments.
5. Slotted section − To measure the signal 6. Probe depth adjustment.
7. Tuning adjustments − To obtain accuracy.
8. Crystal detector − Detects the signal.
9. Matched load − Absorbs the power exited.
10 Short circuit − Provision to get replaced by a load.
11. Rotary knob − To adjust while measuring.
12. Vernier gauge − For accurate results.

## Slide 9
TUNABLE DETECTOR
The above image represents the practical application of this device. It is terminated at the end and has an opening at the other end just as the above one.
The tunable detector is a detector mount which is used to detect the low frequency square wave modulated microwave signals. The Above figure gives an idea of a tunable detector mount.

## Slide 10
To provide a match between the Microwave transmission system and the detector mount, a tunable stub is often used. There are three different types of tunable stubs.
  Tunable waveguide detector
  Tunable co-axial detector
  Tunable probe detector
Also, there are fixed stubs like −
  Fixed broad band tuned probe
  Fixed waveguide matched detector mount
fig:
Photographs of the tunable detector module in a TO39 package

## Slide 11
REFERENCES
  https://www.tutorialspoint.com/microwave_engineering/microwave_engineering_measurement_devices.html
  Das & Das, page 496, Voltmer, page 147
  Tunable Compact Probing Detector with Fast Analysis Time Against Invasive Attacks[IEEE Paper]